## Slide 1: Fluoride Tracer Study
KWWOA 61st Annual Conference
April 9, 2018

## Slide 2: Take Home Message
Water Age – Increases formation of contaminates in tanks, pipes, pipe walls & bulk water that can lead to adverse health effects.
Distribution System is a Reactor That Affects Water Quality
Water Quality Problems: DPB’s, Nitrification, Microbial Survival & Growth and Corrosion
Residence Time
Tracer Studies Gives You Knowledge

## Slide 3: Remediation Critical Control Points for a Tactical Advantage
Wetted Surface cleaning
Air scrubber cleaning
Storage Tank
cleaning
Source Water Protection, Raw Water Line & Storage cleaning
Filtration Media cleaning
Distribution Line Cleaning
Water Contact Time
Wetted Surfaces
4-6 Hrs.
24-96 + Hrs.
Notes: Blue Earth Labs’ Cleaning Mechanisms- Source to Tap. NSF approved Off line & On Line Cleaning chemistries and products for each portion of the infrastructure.

## Slide 4: Water Reactions

## Slide 5: What Contributes to Water Age?
Long Residence time in storage tanks
Fire Flow requirements in new construction Area
Low flow & Lack of Water usage in large diameter piping
Dead end lines with low usage
High Chlorine Demand (Organic & Inorganics)

## Slide 6: Tracer Study
Residual Fluoride
Field Work

## Slide 7: The Problem
Biological and mineral
deposits form on every
wetted surface
The organic matter provides a rich ground for bacteria and biofilms that consume chlorine and chloramine disinfection, lowering residuals, forming DBPs
To maintain residuals, utilities increase chlorine and chloramines that further react with biological matter and form greater levels of DBPs
Eventually, because of the biological interference, residuals cannot be maintained AND DBPs cannot be reduced without distribution system intervention

## Slide 8
WTP
Master Meters
Sample Sites
Tanks

## Slide 9: Equipment Needed
Portable Colorimeter (DR850, 890, 900)
Fluoride SPADNS Reagent
GPS (Smart Phone)
Detailed Sampling Plan, SOP
Sample Site Flushing (Time?)
Stop Watch
Sample Bottles
Adequate Man Power

## Slide 10: Goals
Determine what you want to accomplish?
Determine what other analytical tests you want to run?

## Slide 11: How to ask for approval?
Notify your Regional KY-DOW compliance assistance
Notify your Fluoride Inspector
Do this in writing
Notify the public if necessary, especially if sample sites are located in/around housing

## Slide 12
Direction of Flow
Water Plant

## Slide 13
North Portion of City

## Slide 14
Central Portion of City

## Slide 15
West Portion of City

## Slide 16
East Portion of City

## Slide 17
South Portion of City

## Slide 18: Biological Aspects of Corrosion
BART’s Testing
Iron Bacteria

## Slide 19: QUESTIONS???????
" It's not what you know, it's knowing where to find what you need. "
Contact information:
Bob Cashion 270-790-2726
RKCashion @S4Water.net
The information included in this presentation is proprietary and/or confidential, and protected from disclosure. Do not disseminate, distribute or copy this presentation without the express consent of S4 Water Sales & Service, LLC
“A Team”